### Praesideo Call Station Numeric Keypad PRS-CSNKP

### Architects’ and Engineers’ Specifications

The call station numeric keypad shall have a serial digital interface to connect it to a call station or call station kit with loop through facilities for additional keypads.

The call station keypad shall provide 12 keys (0 … 9, *, #) and an alphanumeric LCD with backlight, that can be configured via the network to provide various functions for the call station, it is connected to.

The configuration shall allow for configuration of the following functions:

- user access to the call station with user number and PIN, configurable for multiple users with time-out and manual lock facilities;

- zone and zone group selection as destinations for calls with up to eight zones or zone groups that can be entered into a string.

The LCD shall give feedback to the user about the selections and the accessibility of the selected zone and zone groups.

The numeric keypad shall get its power from the call station it is connected to.

The unit shall be able to operate at a maximum operating temperature of 45°C.

The numeric keypad shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The call station keypad shall be a Praesideo PRS-CSNKP, manufactured by Bosch Security Systems.